## Slide 1: Hardware Trojan Horse in DNN for misclassification
Boris Bukchin

## Slide 2: AGENDA
Introduction
Experiment setup
Attack framework against NN
Countermeasures
Summary
Notes: In my work I implemented a suggested attack on CNN,
Then tried to find countermeasures.

## Slide 3: INTRODUCTION
Recently, Deep Learning (DL), especially Convolutional Neural Network (CNN), develops rapidly and is applied to many tasks, some of which are extremely safety-critical:
  intelligent surveillance
  autonomous driving

## Slide 4: INTRODUCTION
Due to the latency and privacy problem of cloud computing, embedded accelerators are popular in these safety-critical areas.
Usually, the accelerator or neural network model are provided by third-party companies.
However, the robustness of the embedded DL system might be harmed by inserting hardware/software Trojans into the accelerator and the neural network model.

## Slide 5: Hardware / software Trojan
 | Hardware | Software
Flexibility | Inflexible attack | More flexibility
Availability | Easy | Harder - Usually requires image tampering
Notes: Inflexible: full breakdown
Hard: Data poisoning with glasses – can be tested out, Hidden patterns – hard to implement (even harder with real cameras)

## Slide 6: background - CNN
Convolutional Neural Network for image classification.

## Slide 7: background - Training / interface

## Slide 8: Background -CNN Hardware accelerators

## Slide 9: Background -CNN Hardware accelerators

## Slide 10: Background -CNN Hardware accelerators

## Slide 11: Background -CNN Hardware accelerators

## Slide 12: Background -CNN Hardware accelerators

## Slide 13: Background -CNN Hardware accelerators

## Slide 14: Background -CNN Hardware accelerators

## Slide 15: Experiment Setup

## Slide 16: RESNET18
18 Layers of convolution with skip connections, fully connected layer at the end.

## Slide 17: CIFAR10
The CIFAR-10 dataset contains 60,000 32x32 color images in 10 different classes.

## Slide 18: Pytorch
PyTorch is a machine learning framework based on the Torch library, used for applications such as computer vision and natural language processing.
It is free and open-source software with an easy Python interface.

## Slide 19: Attack framework against NN
Hardware and Software Collaborative Attack

## Slide 20: Attack model
The attackers are the providers of the accelerators and the toolchains.
Hardware Trojan circuits.
Software neural network with Trojan weights.
Input images need not to be manipulated.
On trigger the NN gives specific wrong answers as attacker expects.
On normal operation mode Trojan is hard to detect.
Special algorithm to insert Trojan without influencing the original CNN.

## Slide 21: Motivation
Label-exchanging attack: We exchange the labels of two classes when training the part weights, and two specific classes would be misclassified as the other.

## Slide 22: Trigger
Combinational/Sequential logic.
Sensors.
One bit wire connected to a pin.
Special images.
Normal images in specific sequence.

## Slide 23: Training
We prune the original neural network according to a specific subnet design.
Then we train the sparse neural network with specific training purpose to achieve the attack effect, all inactive weights remain zero.
We keep the active weights unchanged and train the inactive weights only.

## Slide 24: inference
The Trojans are inserted in add part of the processing unit. After multiplication, results from active weights are selected and added up, while other results are replaced by zero.

## Slide 25: Attack Results
The triggered NN is trained to exchange the labels of automobile (1) and frog (6).
The accuracy of normal mode is almost the same as original performance.
High attack success rate.
 | Original Accuracy | Normal Accuracy | Attack Success Rate
Pixel parallelism | 83.8% | 86.7% | 90%
Triggered Mode | Predict | 1 | 6
Label | 1 | 0.4% | 93.6%
 | 6 | 86.6% | 0.1%

## Slide 26: Countermeasures

## Slide 27: Quantization
DNNs exhibit resiliency to quantization in their intermediate results, this is usually used to speed up DNNs and reduce power consumption.
The idea is to check resiliency of the DNN with the trojan – in both triggered and normal mode, in comparison with the original DNN.
Since the trojan NN is not optimal for original dataset we expect to see higher sensitivity to quantization in the trojan NN from the original NN.
If adversarial shows higher sensitivity than original, fine-tuning techniques like quantization can be used as a defense technique as well as efficiency improvements.

## Slide 28: Weight Quantization-results
Didn’t observe significant sensitivity in NN with trojan.
Attack success rate is high with only 3 weight bits.
Accuracy difference stays low.
The result can be explained

## Slide 29: Pruning
Common optimization of DNNs for speed and power consumption is pruning weights.
The idea is to prune the weights of attacker’s network and compare the sensitivity in comparison to original network.

## Slide 30: Pruning-Results

## Slide 31: Pruning + quantization-Results
4-bit quantization

## Slide 32: Hardware trojan detection
Side Channel Signal Analysis
  In proposed attack trigger is added and may affect power.
  Trigger logic may affect timing.
Reverse Engineering
Full Activation of Trojan

## Slide 33: Secure enclave
A secure enclave is a hardware-isolated, trusted execution environment that can run kernels in isolation from other processes or code blocks.
Secure enclave protects the code and data from being tampered with by the attackers during the execution.
Remote attestation enables to prove to a remote party that the enclave and the hardware are “legit”.
Secure enclave can prevent the special training algorithm used by described attack since code and data are encrypted and verified.

## Slide 34: summary

## Slide 35: Summary

## Slide 36: THANK YOU
Boris Bukchin
buboris@campus.technion.ac.il